## Slide 1
REVIEW 1
GridWeave
Multi-Agent Auction-Based Campus Energy Management & Demand Response
PEAS Formulation · Environment & Agent Analysis · Algorithmic Modeling & Search Strategy
Shantharam P · Gauri Nandana S Pai · Akshitha · akolla646
Notes: Introduce GridWeave: a multi-agent simulation of a campus that has less electricity than it sometimes needs. Buildings are agents that forecast and bid; a market decides who gets power; supply agents offer grid, solar and battery power; a coordinator runs the campus in 15-minute slots.

## Slide 2
The Problem & Our Approach
A campus whose supply cannot always meet demand — who gets power, and how is it decided?
420 kW
peak campus demand (09:00–17:00)
250 kW
grid connection — the rest must come from solar + battery
185 kW
critical load (labs, safety) that must stay on
Our approach: a market of autonomous agents
Each building forecasts its own demand and bids for power, separating critical from flexible load
Grid, solar and battery agents offer power with limits and prices
A market allocates supply: critical load first, cheapest sources first
When supply is short, buildings re-bid and give up flexible load (demand response)
After each 15-minute slot, buildings settle against what they really needed
Building agents ×5
bids ↓
Market (auction)
allocations & dispatch ↓
Grid · Solar · Battery
settlement & events ↓
Coordinator (15-min loop)
Notes: Numbers come from our synthetic 5-building campus. The grid alone cannot carry the daytime peak, so the campus depends on solar and a battery, and when any of them fails the market must ration.

## Slide 3
Team & Workstreams
Four workstreams, one system: each is an agent type behind a shared contract
P1 · Building Intelligence
Shantharam P
Synthetic campus demand (5 building types)
Learned demand forecaster (ridge-regression model)
Critical / flexible load classification
Priority, bids & demand response
Settlement against real demand, deferred-energy queue
Shared contracts all agents talk through
P2 · Auction & Market
Gauri Nandana S Pai
Bid validation & multi-criteria scoring
4 allocation strategies incl. welfare-maximising knapsack
Critical-load tiers & emergency rationing
Merit-order dispatch & clearing price
Fairness (Jain's index) & starvation tracking
Re-auction lifecycle
P3 · Energy Supply
Akshitha
Grid agent: time-of-use tariff, outages
Solar agent: generation & weather-aware forecasting
Battery agent: charge level, losses, reserves
Off-peak recharging & cost-based battery pricing
Validated dispatch & energy accounting
Supply events (cloud, outage, price spike)
P4 · Coordination
akolla646
Closed-loop 15-minute coordinator
8 scenarios with scheduled events
3 operating modes for before/after comparison
Campus metrics (service, critical, fairness, cost)
Interactive web dashboard with slot replay
Command-line runner & reports
Notes: Each workstream is one type of agent. They only communicate through shared, validated message types (bids, offers, allocations, dispatch, settlements), so each part can be developed and tested independently.

## Slide 4
PEAS — Building Agent
PEAS Formulation · 3M
The central agent: one per building, all identical code, configured by building type
Performance
Share of real demand served · critical load not served (kWh and events) · expired / curtailed energy · forecast error · energy cost
Environment
Its own stochastic demand (occupancy timetable + noise + spikes) · the market · the coordinator's scarcity signal · 15-minute time slots
Actuators
Submit a bid (requested / minimum / critical kW, priority, willingness to pay) · revise the bid under scarcity · at settlement: serve critical → deferred → flexible; defer or curtail the rest
Sensors
Its own meter (real demand each slot) · scarcity signal · the allocation it received · its own settlement history
Notes: Performance is measured against the demand that actually happened, not against the bid. That is what makes forecasting errors matter. Critical-load shortfall is the most important safety measure.

## Slide 5
PEAS — Market, Supply & Coordinator Agents
PEAS Formulation · 3M
Agent | Performance | Environment | Actuators | Sensors
Market (P2) | Critical load protected · welfare · fairness (Jain) · no building starved | All bids and supply offers for a slot | Allocations to buildings · dispatch requests to sources · clearing price | Bids · supply offers
Grid agent (P3) | Energy delivered · cost | Tariff schedule, outages | Offer kW + price · import power | Time of day, events, dispatch requests
Solar agent (P3) | Renewable energy used | Sun, cloud cover | Offer free solar kW | Time of day, weather events
Battery agent (P3) | Energy delivered at low cost · charge kept in limits | Its charge level, tariffs, outages | Offer kW at cost-based price · discharge · recharge off-peak | Charge level, stored-energy cost, dispatch requests
Coordinator (P4) | Campus service & critical protection · energy conserved · no stuck agent | All agents · scenario event schedule | Advance time · trigger events · run bidding rounds · feed back settlements | Every record, every failure
Notes: Every agent has a clear PEAS. The market is the only agent that maximises a utility function; the battery is the most sophisticated supply agent because it tracks both its charge and the cost of the energy it holds.

## Slide 6
Environment Analysis
Environment & Agent Analysis · 3M
Classifying the task environment the agents operate in
Property | GridWeave | Why
Observable | Partially observable | A building sees only its own meter and the scarcity signal — never other bids or its future demand
Deterministic | Stochastic | Demand has noise and spikes; supply has outages and cloud; outcomes depend on other agents
Episodic | Sequential | Deferred energy, battery charge and each building's deprivation carry consequences forward
Static | Dynamic | Demand, solar and tariffs change every slot; outages happen mid-run
Discrete | Discrete time, continuous values | 15-minute slots; power (kW) and energy (kWh) are real numbers
Agents | Multi-agent: competitive + cooperative | Buildings compete through the market; the market maximises campus welfare
Known | Known rules | Market, settlement and physics rules are fixed and documented
Notes: Partial observability is why the building needs a forecasting model: it must predict its own next 15 minutes to bid. The environment is sequential because postponed energy and battery charge link one slot to the next.

## Slide 7
Agent Analysis — Types & Why Multi-Agent
Environment & Agent Analysis · 3M
Building
Model-based agent with a learned model
Keeps history, deferred-energy queue and deprivation state; predicts demand with a trained model
Market
Utility-based agent
Maximises campus welfare under supply and bid constraints
Battery
Model-based agent
Tracks charge level and the cost of stored energy; prices offers from it
Grid / Solar
Simple rule-based agents
Offer what is physically available at the current price
Coordinator
Orchestrator
Runs the loop, applies events, validates every message
Why multi-agent, not one central optimiser?
Private information: only a building knows its own demand and can forecast it
Decentralised decisions scale: adding a building adds an agent, not complexity
Each part can be replaced behind a contract (market, supply, coordinator)
A simple reflex building (bid its current reading) fails: it under-bids before the morning ramp and cannot carry postponed energy
Notes: The building agent is model-based: it holds internal state and uses a learned model of its demand. The market is the utility-based part. Explain why a simple reflex agent is not enough.

## Slide 8
How the Agents Interact — One 15-Minute Slot
Environment & Agent Analysis · 3M
1
Events
Coordinator applies scheduled events (outage, cloud, price spike)
2
Offers
Grid, solar and battery offer kW and a price
3
Bids
Each building forecasts and bids (critical / minimum / flexible kW)
4
Re-bid
If requests exceed supply, scarcity is announced and buildings trim flexible load
5
Clear
Market allocates power to buildings and dispatch to sources
6
Dispatch
Sources deliver; the battery's charge updates
7
Reality
The slot happens — real demand is revealed
8
Settle
Buildings serve critical first, defer or curtail the rest
9
Feedback
Outcomes carry into the next slot (backlog, charge, deprivation)
Notes: This is the loop the coordinator runs 96 times a day. Every message between agents is a typed, validated object, and the coordinator checks each clearing and dispatch before anything is applied.

## Slide 9
Algorithm 1 — Learned Demand Forecasting
Algorithmic Modeling · 3M
Each building trains its own model on its own history
Model: seasonal linear autoregression
ŷ(t+1) = w · [1, y(t), y(t−1), y(t−2), y(t+1−96), y(t+1−96) − y(t−96)]
Weights fitted by ridge regression on the last 7 days
Recent readings capture momentum; 'same slot yesterday' captures the daily shape
Refitted every 16 slots; recursive for longer horizons
Chosen on development seeds, confirmed on held-out seeds, rolling-origin backtest (no future data)
26%
lower next-slot error than the best statistical baseline
Chart: Next-slot forecast error on held-out data (kW, lower is better)
| LinearAR — learned | EWMA(a=0.6) | Seasonal EWMA | MA(4) | EWMA(a=0.3) | Seasonal naive | MA(8)
MAE (kW) | 3.514 | 4.743 | 5.039 | 6.504 | 7.337 | 8.16 | 9.792
Notes: The learned model is a small supervised regression, trained per building. On held-out data its mean absolute error for the next slot is 3.51 kW, versus 4.74 kW for the best baseline, and the noise floor of the data is about 3.0 kW.

## Slide 10
Algorithm 2 — The Building's Decision Model
Algorithmic Modeling · 3M
Deterministic, explainable rules turn a forecast into a bid
Load classification
critical = min(forecast, max(floor, critical_fraction × forecast))
minimum = critical + comfort floor
Priority score (0–1)
weighted sum of: criticality · building importance ·
urgency of postponed energy · recent deprivation
Willingness to pay
base price → cap, rising with priority,
scarcity and deprivation
Demand response
requested −= scarcity × 0.5 × (requested − minimum)
critical and minimum load are never cut
Notes: Every bid carries an explanation of how its priority and price were computed, so each decision can be traced. Demand response only ever gives up flexible load.

## Slide 11
Search & Optimisation — Market Clearing
Search Strategy · 3M
Who gets power is an optimisation problem solved exactly every 15 minutes
maximise Σᵢ Uᵢ(xᵢ)
subject to Σᵢ xᵢ ≤ available supply
0 ≤ xᵢ ≤ requestedᵢ
xᵢ ≥ criticalᵢ (if supply allows)
Uᵢ is piecewise concave: critical ≫ minimum ≫ flexible (scored by criticality, priority, price, deprivation). Solved as a continuous bounded knapsack — exact, O(N log N).
Strategy | Rule | Role
Proportional | Everyone gets the same fraction | Baseline
Priority-only | Whole requests by priority | Weak baseline
Greedy tiers | Critical → minimum → flexible by score | Critical first
Optimised | Welfare-maximising knapsack | Full GridWeave
Merit-order dispatch
Cheapest source first: solar (free) → battery → grid
Emergency rationing
Supply below total critical load → shared pro rata, every shortfall reported
Battery pricing
Offer = wear cost + cost of stored energy ÷ efficiency (charged off-peak ≈ 12.5/kWh)
Notes: This is where the search and optimisation happens: a constrained welfare maximisation. Because the utilities are concave and piecewise linear, sorting the utility segments and filling greedily gives the optimal solution in O(N log N). Dispatch is a merit-order search over supply offers.

## Slide 12
Algorithm 3 — Battery Scheduling by Price
Algorithmic Modeling · 3M
Charges when power is cheap; the market uses it only when it beats the grid
Chart: Normal scenario, 3 days (hourly)
Recharges 00:00–06:00 at the 5/kWh off-peak tariff, using only spare grid capacity
Tracks the average cost of the energy it holds; offers at wear cost + that cost
After charging it offers at ≈ 12.5/kWh, so the market saves it for the 18/kWh evening peak — or an outage
Result: it refills every night and discharges when it adds value
Notes: The battery agent chooses when to be used through its price. Because its offer reflects the true cost of its stored energy, the market's merit-order dispatch only picks it when the grid is more expensive, which is the evening peak, or when the grid is down.

## Slide 13
Does the Algorithm Matter? Before → After
Algorithmic Modeling · 3M
Same campus, same demand, same events — only the decision-making changes
Chart: Critical load NOT served (kWh) — lower is better
| Daytime grid outage | Cloud + outage + price spike | Supply ≈ half of demand
Equal share (baseline) | 112.5 | 160.9 | 386.9
Critical first | 31.7 | 54.7 | 53.7
GridWeave (full) | 29.9 | 51.5 | 46.8
3.8×
less critical load unserved in a daytime grid outage (113 → 30 kWh)
8×
less under severe scarcity (387 → 47 kWh)
Trade-off: protecting critical load costs some equality — fairness 0.989 → 0.918 under scarcity.
Notes: The biggest gain comes from protecting critical load first. The full GridWeave mode, the welfare-maximising market plus demand response, improves on that by another 6 to 13 percent.

## Slide 14
Assumptions & Anticipated Questions
Q&A · 1M
Modelling assumptions
Synthetic demand: realistic occupancy timetables with noise, not metered data
15-minute slots; power is an average over the slot
Buildings can switch their own flexible loads
Postponed energy must be served within 2 hours
Bids are honest forecasts (the market is not made cheat-proof)
Is this machine learning?
The forecaster is: a supervised model trained per building, tested on held-out data. The market is exact optimisation.
Where is the search?
Market clearing — a welfare-maximising knapsack, exact in O(N log N) — and merit-order dispatch.
What guarantees critical load?
The critical tier serves it fully whenever supply allows; below that it is shared and every shortfall is reported.
What if a forecast is wrong?
Settlement uses real demand: under-forecasts show as shortfall or deferral, over-forecasts as unused allocation.
Notes: State the assumptions before being asked. The full list of viva one-liners is in docs/DESIGN.md section 14.

## Slide 15
Thank you
Questions?
PEAS for 5 agent types, in a partially observable, stochastic, sequential, multi-agent environment
Learned forecasting + exact welfare-maximising market clearing + cost-aware battery scheduling
3.8× less critical load unserved in an outage than an equal-share baseline
Notes: Close by restating the three contributions.